## Slide 1
Window Options

## Slide 2: Table of Contents
Vinyl Colors
Exterior Trims
Interior Trims
Paint
Hardware
Grills
Glass Units
Window Options

## Slide 3: Extruded Vinyl Colours
Many of the vinyl windows produced by Peter Kohler/Kohltech can be made using either white or tan vinyl.
Vinyl Colours

## Slide 4: Exterior Trims
7/8” Brickmould
Nailing Fin
1 ½” Brickmould (also available in extended form)
2” 180 Brickmould
3 ½” Brickmould
3 ½” 180 Brickmould
Exterior Trims
Plain Frame
2” 2 Piece

## Slide 5: Interior Trims
Drywall Return
  ½” Add-on Drywall Return
  ¾” Add-on Drywall Return
Jamb Extension (3/4” thick PVC or Wood/Clad)
  1 ¾” PVC Jamb Extension, stackable
  3 ¾” PVC Jamb Extension, stackable
  ¾” x 2 5/8” Wood Jamb Extension
  ¾” x 3 5/16” Wood Jamb Extension
  ¾” x 4 5/8” Wood Jamb Extension
  ¾” x 5 ¼” Vinyl Clad Wood Jamb Extension
Interior Trims

## Slide 6: Paint
Paint

## Slide 7: Paint (cont.)
Paint
*Custom colours available
upon request

## Slide 8: Paint (cont.)
Paint
We can also match popular colors quickly

## Slide 9: Hardware
White
Tan
Oil Rubbed Bronze
Brushed Nickel
Antique Brass
Hardware

## Slide 10: Grills and Simulated Divided Light (SDL) Bars
Colonial (5/8”)
Georgian (3/4” or 1”)
PVC SDL
(7/8” or 1 1/4”)
5/16” Slimline
Wood SDL
(0.875 “ or 1.22”)
Grills and SDLs

## Slide 11: 5/16” Slimline Grills
Our slimline grills come in 6 colours:
Pewter
Chrome
Brass
Black
Tan
White
Grills and SDLs

## Slide 12: Other Options
Sash Restrictors
Subsill
Flush nosing
Options

## Slide 13: Glass
3 factors can impact glass performance
  Low-E coatings
  Gas filling
  Spacers
Glass

## Slide 14: Low-E Coatings
Ultra thin metallic coating on the glass that reflects heat back to its source – which could be inside or outside
Low-E coating also reflect UV rays, reducing UV damage to furniture and flooring.
Kohltech offers two types of Low-E coating:
  High Solar Gain, Guardian 8070
  Low Solar Gain, Guardian 7138
Glass

## Slide 15: Gas Filling
The heavier the gas, the heat loss across the glass unit.
We use 3 types of gas;
Air : Natural insulator
Argon: An inert gas, heavier than air, better insulator than air
Krypton: Heavier than argon, better insulator than argon, particularly on smaller widths
Glass

## Slide 16: Spacers
Intercept® Tinplate, made with tin-plated steel.
  provides condensation resistance,
  reduced heat loss
  and improves the life expectancy of an IG.
Intercept® Ultra, made with stainless steel,
  offers improved energy efficiency over Intercept® Tinplate.
  Our trademarked Energlas units are produced using this spacer.
Glass

## Slide 17: Spacers
Super Spacer® is a flexible spacer option
  That performs as well as the Ultra spacer.
  Can be bent so it is ideal for shaped windows.
  This spacer is also used for triple glazed units

## Slide 18: Offered IG Units
Energlas® Plus:
  Triple glazed thermopane,
  combines 2 panes of HSG Low-E on surfaces 3 & 5
  both cavities filled with inert gas
  Superspacer
Energlas®:
  Double glazed thermopane,
  Guardian HSG Low-E 0n surface #3
  Argon gas
  Intercept Ultra spacer
Energlas® Plus LSG and Energlas® LSG:
  For year round comfort keeping a home cool in the summer.
  LSG Lo-E is on surface #2 (and #4).
  Offers the lowest U values and solar heat gain coefficients.
Glass

## Slide 19: Offered IG Units
Low-E/Argon:
  Double glazed thermopane
  HSG Low-E on surface #3 with Argon gas filling.
  Tin plated steel spacer
Clear Glass:
  Our standard glazing and most economical choice.

## Slide 20
Kohltech Glass Options
Option | Glazing | Surface 2 | Airspace 1 | Surface 3 | Surface 4 | Airspace 2 | Surface 5 | Unit Size | Spacer
Energlas Plus HSG | Triple Glazed, Lo-E/Argonx2 | Clear | Argon | HSG | Clear | Argon | HSG | 1-3/8" | Superspacer
Energlas Plus LSG | Triple Glazed, Lo-E/Argonx2 | LSG | Argon | Clear | LSG | Argon | Clear | 1-3/8" | Superspacer
Energlas HSG | Double Glazed, Lo-E/Argon | Clear | Argon | HSG | Clear | N/A | N/A | 3/4" | Ultra SS Intercept
Energlas LSG | Double Glazed, Lo-E/Argon | LSG | Argon | Clear | Clear | N/A | N/A | 3/4" | Ultra SS Intercept
LoE Argon HSG | Double Glazed, Lo-E/Argon | Clear | Argon | HSG | Clear | N/A | N/A | 3/4" | Tin Plate Intercept
LoE Argon LSG | Double Glazed, Lo-E/Argon | LSG | Argon | Clear | Clear | N/A | N/A | 3/4" | Tin Plate Intercept
Clear | Double Glazed | Clear | Air | Clear | Clear | N/A | N/A | 3/4" | Tin Plate Intercept
Clear | Triple Glazed | Clear | Air | Clear | Clear | Air | Clear | 1-3/8" | Superspacer
Triple LoE Argon x 1, HSG | Triple Glazed, Lo-E/Argonx1 | Clear | Air | Clear | Clear | Argon | HSG | 1-3/8" | Superspacer
Triple LoE Argon x 1, LSG | Triple Glazed, Lo-E/Argonx1 | LSG | Argon | Clear | Clear | Air | Clear | 1-3/8" | Superspacer
Note: The Supreme Slider Triple glazed has a 7/8" unit size |  |  |  |  |  |  |  |  | 
Other Glass Options in Paradigm: |  |  |  |  |  |  |  |  | 
Bronze Tint, Grey Tint, Obscure, Rain, Satin Deco, Tempered, Laminated |  |  |  |  |  |  |  |  | 

## Slide 21
Kohltech Glass Options
Kohltech Energy Ratings |  |  |  |  |  |  |  | 
Option | Energy Rating | R- Value Centre of glass | R-Value of entire window | U-Value Metric Imperial |  | SHGC | Grills | CR
Energlas Plus LSG | 30 | 8.3 | 5.9 | 1.0 | 0.17 | 0.20 | No | 78
Energlas Plus LSG Grills | 29 | 8.3 | 5.9 | 1.0 | 0.17 | 0.18 | Yes | 78
Energlas Plus HSG | 40 | 7.1 | 5.6 | 1.0 | 0.18 | 0.39 | No | 77
Energlas Plus HSG Grills | 37 | 7.1 | 5.6 | 1.0 | 0.18 | 0.35 | Yes | 77
Triple Low E Argon x 1 LSG | 27 | 5.3 | 4.8 | 1.2 | 0.21 | 0.23 | No | 71
Triple Low E Argon x 1 LSG Grills | 26 | 5.3 | 4.8 | 1.2 | 0.21 | 0.21 | Yes | 71
Energlas LSG | 22 | 4.1 | 3.8 | 1.5 | 0.26 | 0.25 | No | 61
Energlas LSG Grills | 21 | 4.1 | 3.8 | 1.5 | 0.26 | 0.23 | Yes | 61
Energlas HSG | 32 | 3.7 | 3.7 | 1.5 | 0.27 | 0.45 | No | 59
Energlas HSG Grills | 30 | 3.7 | 3.7 | 1.5 | 0.27 | 0.41 | Yes | 59
LoE Argon LSG | 20 | 4.1 | 3.7 | 1.5 | 0.27 | 0.25 | No | 58
LoE Argon LSG Grills | 19 | 4.1 | 3.7 | 1.5 | 0.27 | 0.23 | Yes | 58
LoE Argon HSG | 31 | 3.7 | 3.6 | 1.6 | 0.28 | 0.45 | No | 57
LoE Argon HSG Grills | 28 | 3.7 | 3.6 | 1.6 | 0.28 | 0.41 | Yes | 57
Triple Clear | 29 | 3.2 | 3.4 | 1.6 | 0.29 | 0.44 | No | 62
Triple Clear Grills | 27 | 3.2 | 3.4 | 1.6 | 0.29 | 0.40 | Yes | 62
Clear | 17 | 2.1 | 2.4 | 2.3 | 0.41 | 0.49 | No | 47
Clear Grills | 14 | 2.1 | 2.4 | 2.3 | 0.41 | 0.44 | Yes | 47
Note: All data is for Supreme Casement except for Center of Glass R value which applies specifically to the glass option |  |  |  |  |  |  |  | 
Note: Energlas Products produced in Edmonton use Superspacer and not Ultra SS Intercept |  |  |  |  |  |  |  | 

## Slide 22: Comparison Chart: Clear Glass vs. Low-E
 | Winter Warmth | Heat Gain | Cool in the Summer | UV Protection | Appearance/Clarity | Overall
Clear Glass | Good | Best | Good | Good | Best | Good
HSG 8070(3) | Better | Better | Better | Better | Better | Best
LSG 7138(2) | Best | Good | Best | Best | Good | Better
Glass

## Slide 23: Other Glass Options
Obscure
  Rain Glass
  Satin Deco
  Pinhead
Tempered
Laminated
Tinted
Glass